## Slide 1: Broadcast and multicast routing
A superb presentation from
Joakim Lundmark and Martin Neuman

## Slide 2: What is broadcasting and multicasting?
Broadcasting
  Send to every user in a network
Multicasting
  Send to specific users in a network

## Slide 3: Broadcasting routing
N-way-unicasting
  Most straightforward way to send a broadcast packet, to each destination is to make N copies, one for every user. And then send one to each user.
  Drawback: use a lot of bandwidth for one line.

## Slide 4: Broadcasting routing
Network duplication
  Using the network to create and distribute the copies.
  Flooding, sending to all neighbors in the network.

## Slide 5: Broadcasting routing: Flooding
Uncontrolled flooding
  A fatal flaw with flooding.
    All nodes have two neighbors: Will broadcast packages indefinitely.
    More then two neighbors: Will create a broadcast storm.

## Slide 6: Broadcasting routing: Flooding
Controlled flooding
  SNCF(Sequence-number-controlled flooding)
    Every sender node puts its address and broadcast sequence-number in the broadcast packet.
    Every node has a memory of the address and number of each packet it has duplicated and sent.
    If it receives a packet in the memory it drops the packet. If not it forward-copy it to its neighbors.

## Slide 7: Broadcasting routing: Flooding
Controlled flooding
  RPF (Reverse path forwarding)
    Only sends packet forward if it is received from the next node in the shortest path back to the sender.

## Slide 8: Broadcasting routing
Spanning-Tree Broadcast
    Limits number of sent packets.
    Creates a path for each node to forward received packets. A so called minimum spanning-tree.
    This is done by routing algorithms.

## Slide 9: Broadcasting routing
Creating a center based spanning-tree
    A central node is defined.
    Then all nodes sends a message at the same time towards the center node until they arrive at ether the center node or a node that’s already a part of the tree.

## Slide 10: Broadcasting routing
Spanning-Tree Broadcast

## Slide 11: Multicasting
Specific receivers
  How to identify the receivers of a packet.
  How to address a packet sent to these receivers.
  You can not have all the addresses in the packet because it would be to big.
  A multicast packet is sent by address indirection.
    A single identifier for all the receivers.
    This is done by a multicast group.

## Slide 12: Multicasting
Managing a group
  IGMP(Internet group management protocol).
  Provides the means for a host to inform the router that it wants to join a multicast group.
  It has 3 message types, used for management of the group.
    Membership_Query For joining the group
    Membership_Report For acknowledgements
    Leave_Group For leaving the group

## Slide 13: Multicasting routing algorithms
Multicasting routing using a group-shared tree.
  Similar to the spanning-tree broadcast.
  May use nodes not in the group to “jump” between different parts of the group.

## Slide 14: Multicasting routing algorithms
Multicasting routing using a source-based tree
  Using a RPF(reverse path forwarding) algorithm each node gets its own spanning tree.
  This is better when many users wants to communicate with many users.

## Slide 15: Questions?